## Slide 1
Milling MRR & Power Requirement Estimator
Slab / face milling: table feed, material removal rate and motor power
Group KAI

## Slide 2
Agenda
Group KAI
1. Background
Introduction and types of milling
2. Inputs and method
Parameters, diagram and formulas
3. Results
Worked example and sensitivity
4. Effects
Power flow, torque, chips, wear
5. The tool
Presets, checks and web app
6. Wrap-up
Limits, future work, summary

## Slide 3
Introduction
Group KAI
Milling removes material with a rotating multi-tooth cutter
Machine time and cost depend on how fast material is removed
The spindle motor must supply enough power for the chosen cut
Estimating MRR and power before cutting avoids stalls and tool damage

## Slide 4
Types of milling
Group KAI
Slab milling: cutter axis parallel to the work surface
Face milling: cutter axis perpendicular to the surface
End milling: slots, pockets and contours
This project covers slab and face milling
Note
Same formulas apply to both
Only the engagement geometry differs

## Slide 5
Inputs and outputs
Group KAI
Inputs
Cutter diameter
Number of teeth
Feed per tooth
Cutting speed
Depth of cut
Width of cut
Outputs
Table feed rate
Material removal rate (MRR)
Estimated spindle motor power

## Slide 6
Cutting parameters explained
Group KAI
Symbol | Parameter | Unit
D | Cutter diameter | mm
z | Number of teeth | count
fz | Feed per tooth | mm/tooth
Vc | Cutting speed at the cutter edge | m/min
ap | Depth of cut (axial) | mm
ae | Width of cut (radial) | mm

## Slide 7
2D diagram: cutter engagement (top view)
Group KAI
Workpiece
D = 100 mm
ae = 70 mm
Feed direction
Reading the diagram
Orange ring: cutter with 8 teeth
Grey area: workpiece
D: cutter diameter
ae: width of cut, 70% of D
ap = 3 mm is the depth into the page
vf moves the table along the feed direction

## Slide 8
Formulas
Group KAI
Spindle speed
n = 1000 · Vc / (π · D)
Table feed rate
vf = fz · z · n
Removal rate
MRR = ae · ap · vf / 1000
Cutting power
Pc = MRR · kc / 60 000
Motor power
Pm = Pc / η
Spindle torque
T = 9550 · Pc / n

## Slide 9
Worked example: medium-carbon steel
Group KAI
Parameter | Value
Cutter diameter D | 100 mm
Teeth z | 8
Feed per tooth fz | 0.15 mm
Cutting speed Vc | 180 m/min
ap / ae | 3 mm / 70 mm
kc / efficiency | 2200 N/mm² / 80%
Result | Value
Spindle speed | 573 rpm
Table feed rate | 688 mm/min
MRR | 144 cm³/min
Cutting power | 5.29 kW
Motor power | 6.62 kW
Torque | 88 N·m

## Slide 10
Cutting force by material
Group KAI
Workpiece material | kc (N/mm²)
Aluminium alloy | 700
Brass / bronze | 800
Grey cast iron | 1100
Titanium (Ti-6Al-4V) | 1400
Mild steel (1020) | 2000
Medium-carbon steel (1045) | 2200
Stainless steel (304) | 2400
Alloy steel (4140) | 2600

## Slide 11
Effect of feed per tooth
Group KAI
fz (mm/tooth) | Feed rate (mm/min) | MRR (cm³/min) | Motor power (kW)
0.06 | 275 | 58 | 2.65
0.10 | 458 | 96 | 4.41
0.15 | 688 | 144 | 6.62
0.20 | 917 | 193 | 8.82
0.25 | 1146 | 241 | 11.03
Same setup as the worked example. Power rises in direct proportion to feed, so a 7.5 kW motor limits fz to about 0.17 mm.

## Slide 12
Power flow and efficiency
Group KAI
Cutting power Pc is what the cut itself consumes: 5.29 kW
The motor also feeds gearbox and spindle losses
Motor power = Pc / η, with η = 80%: 6.62 kW
Motor load = required power / rated power
Example
7.5 kW motor: 88% load
Above 80% leaves little headroom

## Slide 13
Torque and spindle speed
Group KAI
Torque T = 9550 · Pc / n, in N·m with Pc in kW
Example: 9550 × 5.29 / 573 = 88 N·m
Low rpm with heavy cuts is torque-limited
High rpm with light cuts is power-limited
Tip
Check the machine torque curve
Gear range matters on older machines

## Slide 14
Chip thickness and feed per revolution
Group KAI
Mean chip thickness hm = fz · √(ae / D)
Example: 0.15 × √0.7 = 0.126 mm
Feed per revolution = fz · z = 1.2 mm/rev
Chips thinner than 0.05 mm cause rubbing and heat
Guidance
Raise fz if chips are too thin
Cutting time for 300 mm: about 26 s

## Slide 15
Tool wear and rake angle
Group KAI
Condition | kc factor | Motor power (example)
New, sharp tool | × 1.00 | 6.62 kW
Moderate wear | × 1.15 | 7.61 kW
Worn tool | × 1.30 | 8.60 kW
Rake angle 0° | × 1.09 | 7.21 kW
Rake angle 12° | × 0.91 | 6.02 kW
Worn tools can push a comfortable cut past the motor rating, so plan for wear.

## Slide 16
Presets in the tool
Group KAI
Preset | D | z | fz | Vc | ap | ae
Steel roughing | 100 | 8 | 0.18 | 160 | 4 | 70
Aluminium finishing | 80 | 6 | 0.10 | 600 | 0.5 | 60
Stainless steel | 63 | 5 | 0.12 | 120 | 2 | 45
Titanium | 63 | 6 | 0.10 | 60 | 2 | 40
Cast iron | 125 | 10 | 0.20 | 140 | 3 | 90
Units: D, ap, ae in mm; fz in mm/tooth; Vc in m/min.

## Slide 17
Safety checks and warnings
Group KAI
Width of cut above cutter diameter
Required power above the motor rating
Motor load above 80%
Depth of cut large compared with diameter
Chips thinner than 0.05 mm

## Slide 18
The web application
Group KAI
Live results
All outputs update as you type
3D simulation
Spinning cutter, sparks and coolant
Warnings
Overload, thin chips and ae above D
Presets
Steel, aluminium, stainless, titanium, cast iron
Power chart
Motor power against feed per tooth
Themes
Light and dark, responsive to 4K

## Slide 19
Limitations and future work
Group KAI
Uses handbook cutting-force values, so results are estimates
Assumes a constant kc and straight-line engagement
Next: more materials and imperial units
Next: report export and saved jobs

## Slide 20
Summary
Six cutting inputs give feed rate, MRR and motor power instantly
The diagram shows how width of cut sets cutter engagement
Wear, rake angle and chip thickness refine the estimate
Project by Group KAI. Thank you!